## Slide 1: Introduction into the Physics and Technology of Particle Accelerators
Rüdiger Schmidt – CERN / TU Darmstadt
Graduiertenkolleg
10 October- 14 October 2011
Home page: http://rudi.home.cern.ch/rudi/
E-mail: rudiger.schmidt@cern.ch

## Slide 2: Literature on particle accelerators
Literature
Physik der Teilchenbeschleuniger und Synchrotronstrahlungsquellen, Klaus Wille, Teubner Verlag, Studienbücher, 2. Auflage 1996 (exists also in English)
Helmut Wiedemann, Particle Accelerator Physics
Edmund Wilson, An Introduction to Particle Accelerators
Proceedings of CERN ACCELERATOR SCHOOL (CAS), Yellow Reports, für viele Themen in der Beschleunigerphysik, General Accelerator Physics, and topical schools on Vacuum, Superconductivity, Synchrotron Radiation, Cyclotrons, and others… http://schools.web.cern.ch/Schools/CAS/CAS_Proceedings.html
5th General CERN Accelerator School, CERN 94-01, 26 January 1994, 2 Volumes, edited by S.Turner
Special topics
Superconducting Accelerator Magnets, K.H.Mess, P.Schmüser, S.Wolff, WorldScientific 1996
Handbook of Accelerator Physics and Engineering, A.W.Chao and M.Tigner, World Scientific, 1998
A.Sessler, E.Wilson: Engines of Discovery, World Scientific, Singapur 2007
Conferences and Workshops on accelerator physics (EPAC, PAC, IPAC, …)

## Slide 3: Overview
Accelerator Physics: An Introduction
Particle accelerators: From basic to applied research
Development of accelerators
Example for accelerators
Description of the particle dynamics - Basics
Magnetic fields and focusing of particle beams
Movement of charged particles in a magnetic field
Betatron function and optical parameters
Acceleration and longitudinal phase space
Cavities for particle accelerators
Example for collective effects: space charge
LHC at CERN

## Slide 5: Chapter 1 Accelerator Physics: Introduction
Rüdiger Schmidt (CERN) – 2011 - Version E1.0

## Slide 6: Overview
What is a particle accelerator?
Relativistic kinematics: Velocity and Energy
Acceleration of particles
Deflection of particles
What is accelerator physics?

## Slide 7: What is a particle accelerator?
Definition
  CAMBRIDGE DICTIONARY: A particle accelerator is a machine which makes extremely small pieces of matter travel at very high speeds, so that scientists can study the way they behave
Particle accelerators are the most complex research instruments that are used in research and development in Physics, Chemistry, Biology, Medicine, Archaeology, Energy research and other areas
Particle accelerators are also widely used in industry

## Slide 8: What particles?
From 1920 until today…..
Electrons
  Restmass m0  c2 = 511 keV, elementary particle with negative charge e0=1.602  10-19 C
Positrons
  Restmass m0  c2 = 511 keV, elementary particle with positive charge e0 =1.602  10-19 C
Protons
  Restmass m0  c2 = 938 MeV, no elementary particle (Quarks and Gluons)
  Positive charge e0 = 1.602  10-19 C
Antiprotons
  As protons made of quarks, mass as protons, negative charge
Ions (Deuterons to Uranium)
  Charge is a multiple of the elementary charge, mass of 2mProton to Uranium
  Stable und unstable Ions (Beta Beams)
Ideas for the future
m mesons / Muon– Collider
  elementary particle as e+/e-, restmass m0  c2 = 106 MeV, Charge e0 =1.602  10-19 C
  lifetime: 2.2  10-6 s in rest system. Im lab system: LAB =   RS

## Slide 9: Parameters of a particle
The energy varies with the speed
The spin is not considered in the context of this lecture, but will be discussed in some of the afternoon presentations
Restmass m0
Charge q
Spin
velocity vx, vy, vz
Position in space x, y, z
z
x
y

## Slide 10: Acceleration and deflection of particles: Lorentz force
The force on a charged particle is proportional to the charge, the electric field, and the cross product of the velocity vector and magnetic field:
For an electron, positron, proton,... the charge q is the elementary charge:
Acceleration is only by electric fields, in the magnetic field particles cannot be accelerated :

## Slide 11: Energy gain of charged particles
Example: a charged particle is accelerated in the potential.
Relationship between voltage and electric field:
Energy gain of charged particle:
The energy gain of a charged particle is proportional to the voltage and the charge of the particle.

## Slide 12: Acceleration of an electron in the electric potential
e.g. capacitor
U = 10000 V
d = 1 m
q = e0
E = 10000 eV
+
-
+
Definition of „eV“: a particle with the charge e0, travelling through an electric field with a potential difference of one volt gains an energy of one eV (electronvolt).
1 eV = 1.602  10-19 Joule
The energy gain is independent of the energy and velocity of the particle, and the distance between the two plates
Enew = Eold + E
d = 1 m
U = 10000 V

## Slide 13: Relativistic kinematics: speed and energy
The speed of the particles at high energy approaches the speed of light.
The speed of light may not be exceeded.
Assumption: A particle with mass m0 is moving at the speed v regarding the laboratory system.

## Slide 16: Deflecting force on a relativistic charged particle

## Slide 17: Deflection by an electrical field (animation)

## Slide 18: Magnetic fields - electric fields
For the acceleration of charged particles electric fields are used
Magnetic fields are used for the deflection of particles and for focusing particle beams.
There are also some applications for electrostatic fields for the deflection of particles, e.g.:
  Beam separation for particles with opposite charge in a storage ring
  Feedback systems: it is necessary for high beam intensity to deflect individual bunches for beam stabilisation. Electric fields are used
  Injection and extraction kicker magnets use electric fields

## Slide 19: Particle motion in a magnetic field
Protons
Antiprotons
B
B
A circular accelerator for two beams with equal particles requires magnets with opposite field direction.
Therefore many colliders are operating with particles and antiparticles (p-antiproton, e+e-)

## Slide 20: Are accelerators always “accelerating” particles?
  here: accelerating – increasing the energy
True for the most accelerator... but not for all
You would call a TV not an accelerator, although it accelerates electrons with a voltage of some kV
Storage rings are accelerators where particles are stored (the particle energy remains constant in many of such "accelerators")
For accumulating positrons and antiprotons
For colliding two proton beams (injection at collision energy, e.g. CERN ISR)
Accelerator to produce synchrotron radiation (one of the most important types of accelerators), often without acceleration of the particles
Accelerator where particles are directed on a target
For the production of neutrinos or other particles
The production of antiprotons works with protons, which are directed on a target with an energy of several GeV
Accelerator where particles are slowed down
The antiprotons produced in a target have a kinetic energy of a few hundred MeV, and are slowed down for experiments with a few eV (CERN - AD) - e.g. for the production of anti - hydrogen

## Slide 21: What is Accelerator Physics and Technology?
The physical and technical basics to design, develop, build and operate a particle accelerator
Electromagnetism
Radiation Physics
Particle physics
Relativity
Thermodynamics
Mechanics
Quantum mechanics
Physics of non-linear systems,
Solid state physics
Surface science and vacuum physics
Also: Mechanical engineering, electrical and electronics engineering, computer science, civil engineering, including surveying

## Slide 22: Accelerator Technology Accelerator Physics
Sources for the production of particles
Structures for particle acceleration (cavity resonators)
Magnets for particle deflection
Cryogenics for superconducting magnets and cavities
High vacuum systems for storage rings
  to store particles for many hours in a storage ring
Beam instrumentation and control
Kicker magnets
  to inject and extract particles
Linear transverse beam dynamic (optics)
Nonlinear transverse beam dynamics
Longitudinal beam dynamics
Synchrotron radiation
Collective effects
Particle interaction with matter

## Slide 23: Applications of particle accelerators
Particle physics: CERN, FERMILAB, JPARC, JLAB, KEK, …
Application of synchrotron radiation: z.B. ESRF, DESY, SLAC, ANKA (KIT), ….
  Chemistry, Biology, Physics, etc
Nuclear physics: S-DALINAC, GSI, SNS (Oak Ridge, USA), Mainzer Mikrotron MAMI, ….
Medical applications: GSI - Heidelberg, PSI (Schweiz), …
  Production of radioisotopes
  Irradiation of patients, e.g. for treating tumours
Archaeology, age dating, environmental research (e.g. Vienna - VERA)
Technology related to energy research: Fusion (IFMIF), Energy Amplifier, Accelerator Driven Spallation (ADS) such as MYRRHA in Belgium
Industrial applications