## Slide 1: Chapter 2 Particle accelerators: From basic to applied research
Rüdiger Schmidt (CERN) – 2011 - Version E1.0

## Slide 2: Scientific motivation for accelerators
The interest in accelerators came first from nuclear physics
Particles from radioactive decays have energies of up to a few MeV. The interest was to generate such particles, e.g. to split the atomic nuclei, which was for the first time done in 1932 with a Cockroft-Walton Generator.
Ernest Rutherford 1928:
I have long hoped for a source of positive particles more energetic than those emitted from natural radiaoactive substances
Cockcroft, Rutherford and Walton soon after splitting the atom
http://www.phy.cam.ac.uk/alumni/alumnifiles/Cavendish_History_Alumni.ppt

## Slide 3: Dimensions in our universe
Typical dimension of atomic and subatomic matter:
Distance of atoms in matter: 0.3 nm = 3•10-10 m
Atomic radius: 0.1 nm = 1•10-10 m
Proton / Neutron radius: 1•10-15 m
Classical electronenradius: 2.83•10-15 m
Quark: 1•10-16 m
Range of strong interaction : < 1•10-15 m
Range of Weak interaction : << 1•10-16 m
Mass of an electron: 9.11•10-31 kg
Mass of a proton : 1.673•10-27 kg

## Slide 4: Particle energy and basic research
For studies of the structure of the material, “probes“ are required which are smaller than the structure to be examined, for example: Light microscope ( - Quants with an energy of about 0.25 eV)
  Electron microscopes
  Particle accelerators – the probe is the particle
  Particle accelerators – the probe is the radiation emitted by the particles (light quantum with an energy of some eV up to few MeV)
  Particle accelerators - the probe is a neutron. Neutrons are in general generated with intense high energy proton beams on a target
The production of new particles requires particles with enough energy
Examples: Particle accelerators
Cosmic rays

## Slide 5: Particle energy and basic research
Extension of the probe to study material structures
Light, typical wavelength: 500 nm = 5•10-7 m
For particles, the De Broglie wavelength becomes smaller with increasing
kinetic energy:

## Slide 6: Research on small structures requires high energy
Example for the De Broglie wavelength:
Kinetic energy of a proton:
De Broglie wavelength for the proton:
Kinetic energy of an electron:
De Broglie wavelength for the proton:

## Slide 8: Energy spectrum: Cosmic radiation and accelerators
Cosmic radiation is free of charge!
Investment for particle physics with accelerators: ~GEuro
But:
Cosmic rays at 1 TeV: <0.001 particles / m2 / sec
LHC 7 TeV:
>1026 protons / m2 / sec
LHC am CERN

## Slide 9: Creation of secondary particles in fixed target experiments
An accelerator that directs particles on a target:
Particles from the accelerator with the kinetic energy E and
mass m0
Particles in the target with mass m1
Conservation of momentum and energy
Secondary particles from the collision with momentum p and mass m

## Slide 10: Production of secondary beams
Sekundary beam:
  Positrons
  Antiprotons
  Neutrinos
  Myons
  Pions
  Kaons
Primary beam
Target
Magnet
Parameters: Beam Intensity and Particle type

## Slide 11: Production of “new” particles with colliding beams
Accelerator where two particles collide:
Conservation of momentum and energy:
New particle with momentum = 0
and mass m0
Note: to produce a Z0 needs e+ e- beams with each about 46 GeV. For the production of W+ W-pair, the accelerator requires the double energy (conservation of charge!)
Particles from the accelerator with the kinetic energy E and
mass m0

## Slide 12: Particle physics: cross section
Approximation (example): to investigate the inside of a proton, a high-energy proton beam collides with another proton
„Protonradius“: ~10-15 m
„Area“ is in the order of: ~10-30 m2
Definition: Barn  10-24 cm2 = 10-28 m2
Diameter of the beam: 10-3 m (1 mm)
Number of protons in the beam: 1014
Probability, that a proton in the beam collides with another proton: 10-30 m2 / 10-6 m2
In order to obtain a collision rate of 1 Hz, about 1024 colliding protons per second are required
Small cross section of the beams
Intense particle beams

## Slide 13: Colliding Beams: Energy and Luminosity
e+e- storage rings: LEP-CERN until 2001, B-Factories at SLAC and KEK (USA, JAPAN)
e+e- linear accelerators (Linacs): - being discussed – ILC (Int. Linear Collider) und CLIC – CERN
Proton-Proton: ISR until 1985, und LHC – CERN from 2008
Proton-Antiproton Collider: SPS – CERN until 1990, TEVATRON – FERMILAB (USA) just finished
e+ or e- / Proton: HERA (DESY) – until 2007
Number of "new particles"“:
  LEP (e+e-) : 3-4 1031 [cm-2s-1]
  Tevatron (p-pbar) : 3 1032 [cm-2s-1]
  B-Factories : >1034 [cm-2s-1]
  LHC nominal : 1034 [cm-2s-1]
  LHC today: 3-4 1033 [cm-2s-1]

## Slide 14: Luminosity
L = N2 f n b / 4p s x s y
N ......... Number of particle per bunch
f ......... Revolution frequency
nb......... Number of bunches
x s y ... Transverse beam dimensions at collision point (Gaussian)
Protons N per bunch: 1011
f = 11246 Hz, Number of bunches: nb = 2808
Beam size σ = 16 m
L = 1034 [cm-2s-1]
Example for LHC

## Slide 16
Z0 Teilchen bei LEP

## Slide 17: Energy and power of a particle beam
The energy that is stored in a particle beam is given by:
The power in the beam is given by:
For many new projects high power of the beam is of crucial importance (power exceeding one MW).

## Slide 18: Energy stored in the beam
Chart: Momentum [GeV/c]
| 26 | 100 | 250 | 315 | 450 | 450 | 450 | 450 | 450 | 920 | 900 | 7000 | 7000
Stored Energy MJ | 3 | 0.02 | 0.9 | 0.04 | 2.4 | 0.66667 | 2.5 | 25 | 2.5641 | 2.67 | 1.6 | 362 | 9800

## Slide 19: Importance of particle physics for the development of accelerators
The driving force behind the development of accelerators came from particle physics
Particle physicists are still the most demanding user of particle accelerators
This is starting to change – now progress in accelerator physics is being also driven by other users

## Slide 20: The use of Accelerators (R.Aleksan)
This « market » represents ~15 000 M€ for the next 15 years, i.e. ~1000M€/year
Projects | Science field | Beam type | Estimated cost
LHC | Particle Physics | proton | 3700M€
FAIR | Nuclear Physics | Proton /ion | 1200M€
XFEL | Multi fields | electron aphoton | 1050M€
ESS | Multi fields | Proton aneutron | 1300M$
IFMIF | Fusion | Deuteron aneutron | 1000M€
MYRRHA | Transmutation | Proton aneutron | 700M€
In past 50 years, about 1/3 of Physics Nobel Prizes are rewarding work based on or carried out with accelerators

## Slide 21
Clinical accelerators
Industrial accelerators
Total accelerators sales increasing more than 10% per year
Courtesy: R. Aleksan and R. Hamm
radiotherapy
electron therapy
hadron (proton/ion)therapy
ion implanters
electron cutting & welding
electron beam and X-ray irradiators
radioisotope production
…
Application | Total systems (2007) approx. | System sold/yr | Sales/yr ($M) | System price ($M)
Cancer Therapy | 9100 | 500 | 1800 | 2.0 - 5.0
Ion Implantation | 9500 | 500 | 1400 | 1.5 - 2.5
Electron cutting and welding | 4500 | 100 | 150 | 0.5 - 2.5
Electron beam and X-ray irradiators | 2000 | 75 | 130 | 0.2 - 8.0
Radioisotope production (incl. PET) | 550 | 50 | 70 | 1.0 - 30
Non-destructive testing (incl. security) | 650 | 100 | 70 | 0.3 - 2.0
Ion beam analysis (incl. AMS) | 200 | 25 | 30 | 0.4 - 1.5
Neutron generators (incl. sealed tubes) | 1000 | 50 | 30 | 0.1 - 3.0
Total | 27500 | 1400 | 3680 |